## Slide 1: Search Towards an Advanced Deep learning Algorithm for MRI Quantitative Susceptibility Mapping (QSM) with Magnetic Anisotropy
Presented by:
Tasmin Khan Student ID: 1906055
EEE 400
Supervisor:
Dr. Maruf Ahmed
Assistant Professor
EEE, BUET
Presentation Date: 16 March 2025
Bangladesh University of Engineering and Technology
Department of Electrical and Electronic Engineering

## Slide 2: How is an MRI image created?
Magnetic Response of the tissues are measured
What kind of response is measured,
makes different modalities
Measuring magnetic susceptibility forms QSM (Quantitative Susceptibility Mapping)

## Slide 3: Why is QSM needed?
Magnetic
Susceptibility
Paramagnetic
Iron
Alzheimer’s
Diamagnetic
Calcium
Biological tissues
Parkinson’s
Multiple Sclerosis
Hemoglobin
Iron Accumulation -> positive susceptibility

## Slide 4: How is QSM image formed?
MRI signals
Phase
Signals
Phase processing
Phase map, ϕ
Dipole inversion
Susceptibility
map (QSM), χ
Φ
χ

## Slide 5: Equation for Dipole Inversion
= D · χ
Φ Phase map
γ and t Scan parameter
χ Susceptibility map
D Dipole kernel
D (k) = −

## Slide 6: Algorithms to solve inversion
Traditional Iterative Approach
Physics-based constraints and iterative regularization
Cons:
Computationally expensive
Slow converge
Parameter Tuning
Sensitive to noise
Single orientation
Multi orientation
COSMOS
STI
iLSQR
MEDI
TKD

## Slide 7: Physics Guided Architecture with CNN
Learning parameters of physics-based equations via CNN
Pros:
Better reliability
Cons:
Computationally expensive
Struggles to capture global dependencies
Needs additional input i.e. dipole kernel
Key Models
LPCNN
VaDNI
MoDL

## Slide 8: Pure deep Learning based algorithms
Conventional Model Architecture
Learning direct mappings between phi images and chi maps
Pros:
Better Generalization
Artifact and noise Reduction
Faster Reconstruction
Cons:
Local Perceptive Field
Dependent on data diversity
Key Models
QSMnet
IR2QSM
xQSM
DIAM-CNN

## Slide 9: Transformer based Architecture
Self Attention Mechanism:
Weighs importance of different parts of input data considering all the parts simultaneously
Current application:
CT scan reconstruction
MRI image segmentation
Pros:
Captures long range dependency
Cons:
Needs a large number of data
May need architecture modifications to capture fine details

## Slide 10: Data processing
Processing raw MRI scans to trainable dataset is a critical and complex yet time-intensive part of the pipeline.
Chan, K.-S., & Marques, J. P. (2021). SEPIA—Susceptibility mapping pipeline tool for phase images. NeuroImage

## Slide 11: Raw MRI scan
First RF pulses are applied on the tissues
Complex (magnitude and phase) tissue signals are received
Echo time is the time between RF pulse and the signal received
Multiple echo times capture the phase changed at different times
Shorter echo times give clearer magnitude images
Longer echo times give more detailed phase image

## Slide 12: Magnitude Image Phase Image
Extracted from
RAW MRI scans
Image viewing Tool: ITK-SNAP

## Slide 13: Image Registration
Scans acquired in different orientations.
Transformation to get the same subject’s frame of reference for all the images.
Needs scaling, rotation, translation, and shearing to match.
Algorithm: Affine transformation

## Slide 14: Registration Matrix
4 by 4 Affine registration matrix
Example matrix derived
0.9201344417 | -0.1888734378 | 0.3360556196 | 12.26195665
0.2858273205 | 0.9078385504 | -0.2939861069 | -3.219740788
-0.2528859749 | 0.367988024 | 0.8904688316 | -18.53737804
0 | 0 | 0 | 1

## Slide 15: Brain Extraction to discard invalid regions
From MRI Magnitude images Tools: FSL BET Figure: ITK-SNAP

## Slide 16: Phase Unwrapping Background Phase Removal
Done for each echo
Algorithm: Laplacian phase unwrapping and VSHARP (Variable Sophisticated Harmonic Artifact Reduction)

## Slide 17: Multiple echoes
Normalizing each echo by 2π · γ · TE · B
γ constant, TE echo time, B magnetic field
Averaging over 5-7 echoes
Final phase map

## Slide 18: Magnetic Susceptibility Anisotropy
Accounts for Directional dependence of magnetic property based on orientation
Isotropic Anisotropic

## Slide 19: Susceptibility Reconstruction
Phase Reconstruction from multiple orientation phase images
Algorithm: aSTI (Anisotropic Susceptibility Tensor Imaging)
χ13 χ23 χ33

## Slide 20: Magnetic Anisotropy
χadjusted =
Adjusting χ map voxel by voxel for each orientation
Orientation 1
Orientation 2
Difference

## Slide 21: First Model: MoDL
Output
Input
First Iteration
Second Iteration
Third Iteration
L1 Loss
Physical Block
Prepares the input for next iteration
CNN block
Learns the Parameters of iterative equations
Trained for 35 hours
Batch size was limited to only 2
Highest patch size could be 48×48×48

## Slide 22: Result
Target Generated Difference
MoDL-QSM | RMSE | SSIM
Training | 68.42 | 0.8306
From Paper | 67.91 | 0.8446
Structural Similarity Index
Ref: Feng Et al. MoDL-QSM: Model-based deep learning for quantitative susceptibility mapping, 2021

## Slide 23: But do we need 3D images?
3D QSM
Huge computation resources
Lengthy Training time
Limited to smaller patch size
Unnecessary for clinical diagnosis
2D QSM
Minimal computation resources
Reduced Training time
3× bigger patch size
Sufficient for clinical diagnosis

## Slide 24: Time to build a 2D dataset
Axial Coronal Sagittal
Input Phimap
Target Chimap
Slicing Across the Axial, Coronal and Sagittal planes
Making sure planes too close are not selected
Slicing size chosen to be 128× 128×128

## Slide 25: Invalid Slice
Slices with more than 80% non-brain region are discarded

## Slide 26: Second Model: Swin-Unet
Batch size increased to 10
Each epoch requires
around 20 minutes to train
2D Image size was
128× 128×128
Reference: Cai, Y. Et al. “Swin unet3d: a three-dimensional medical image segmentation network combining vision transformer and convolution.”, 2023

## Slide 27: Training Log
Abnormally low loss metric
Saturates in Validation loss in very few epochs
Model practically memorizes the data
Loss metric vs Epoch plot
Loss
Epoch Number

## Slide 28: Why is this happening?
Potential Reasons:
Transformers focuses on long-range dependencies, but not so much on fine details or local dependency.
Dataset consisted of different orientations of the same subject; they differ in fine details due to anisotropy but greater structure is the same.
Repetitive data leads to model overfitting to train data.
Model architecture might be too complex for the available data.

## Slide 29: Future work
Using a simpler pure deep learning model without heavy transformer
Incorporation of Generative Adversarial Networks (GANs) as a post-processing step to refine the output of the model
Expanding Data Augmentation Techniques such as inverting or scaling the susceptibility

## Slide 30: References
Liu, C., Li, W., Tong, K., Yeom, K. and Kuzminski, S. “Susceptibility-weighted imagingand quantitative susceptibility mapping in the brain.” J. Magn. Reson. Imaging, volume 42,no. 1:pp. 23–41, Jul 2015. Epub 2014 Oct 1
eng, R., Zhao, J., Wang, H., Yang, B., Feng, J., Shi, Y., Zhang, M., Liu, C., Zhang,Y., Zhuang, J. and Wei, H. “MoDL-QSM: Model-based deep learning for quantitativesusceptibility mapping.” NeuroImage, volume 240:p. 118376, 2021
aswani, A., Shazeer, N., Parmar, N., Uszkoreit, J., Jones, L., Gomez, A.N., Kaiser, andPolosukhin, I. “Attention is all you need.” Advances in Neural Information ProcessingSystems, volume 30, 2017
Liu, Z., Lin, Y., Cao, Y., Hu, H., Wei, Y., Zhang, Z., Lin, S. and Guo, B. “Swintransformer: Hierarchical vision transformer using shifted windows.” arXiv preprintarXiv:2103.14030, 2021
Wei, H., Zhang, Y., Gibbs, E., Chen, N.K. et al. “Joint 2d and 3d phase processing forquantitative susceptibility mapping: Application to 2d echo-planar imaging.” NMR inBiomedicine, volume 30, no. 4, 2016
Shi, Y., Feng, R., Li, Z. et al. “Towards in vivo ground truth susceptibility for single orientation deep learning qsm: A multi-orientation gradient-echo mri dataset.” NeuroIm age, volume 261:p. 119522, 2022
Li, W., Wu, B., Avram, A.V. and Liu, C. “Magnetic susceptibility anisotropy of human brain in vivo and its molecular underpinnings.” NeuroImage, volume 59, no. 3:pp. 2088 2097, 2012
Cai, Y., Long, Y., Han, Z. et al. “Swin unet3d: a three-dimensional medical image segmen tation network combining vision transformer and convolution.” BMC Medical Informatics and Decision Making, volume 23:p. 33, 2023
….. and more

## Slide 32: Equation for Dipole Inversion
∆B(r) = D(r)∗χ(r)
∆B(k) = D(k)· χ(k)
χ(k) = ∆B(k) / D(k)
D (k) = −
Φ Phase map
Magnetic Field perturbation
γ and t Scan parameter
χ Susceptibility map
D Dipole kernel

## Slide 33: Comparison of metrics
Model | RMSE | SSIM
MoDL-QSM(Training) | 68.42 | 0.8306
MoDL-QSM(From Paper) | 67.91 | 0.8446
AutoQSM | 69.40 | 0.8549
QSMnet | 55.07 | 0.8759
STAR-QSM | 79.57 | 0.8180

## Slide 34: Outline of Presentation
Background and theory
References
Literature Review of algorithms
Training
Results
Data processing
Conclusion